## Slide 1: Please attribute as SimpleITK Fundamental Concepts
This work is copyrighted by the NumFOCUS
It is distributed under a Creative Commons Attribution 4.0 International License: https://creativecommons.org/licenses/by/4.0/

## Slide 2: SimpleITK Fundamental Concepts
Marina Torch Tower in Dubai (Wikimedia commons Creative Commons Attribution-Share Alike 3.0 Unported).
With a Solid Foundation
The Sky is the Limit

## Slide 3: Transforms
All global domain transformation are of the form*:
*Except translation.
Transforms Images Resampling Registration

## Slide 4: Transforms
Free-Form Deformation (local domain):
You set:
  Spline order (default is cubic)
  Number of grid points per axis (mesh size)
  Spatial domain manually: origin; physical dimension; direction cosine matrix image based: BSplineTransformInitializerFilter
Transformation is identity outside the user defined domain.
sparse grid of control points with uniform spacing,
B0..3
cubic B-spline basis functions.
Transforms Images Resampling Registration

## Slide 5: Transforms
Displacement Field (local domain):
  Dense set of vectors representing the displacement in a given spatial domain.
You set:
  Spatial domain and deformation: manually: origin; physical dimension; direction cosine matrix; vector values. image based: vector image which is emptied of its contents.
Transformation is identity outside the user defined domain.
Transforms Images Resampling Registration

## Slide 6: Transforms
Composite transformation:
  Represents multiple transformations applied one after the other. T0(T1(T2(…Tn(p)...)))
Stack based semantics – first in last applied. composite_transform = sitk.Transform([T0,T1]) composite_transform.AddTransform(T2)
When used as the optimized transformation in registration (SetInitialTransform), only the parameters of the last transformation, Tn, are optimized.
Transforms Images Resampling Registration

## Slide 7: Images
An image is defined by:
  Pixel type + spatial dimensionality.
  Physical region in space occupied by the image as specified by: origin, spacing, size, and direction cosine matrix.
Transforms Images Resampling Registration

## Slide 8: Images
Exactly the same intensities, but in a different physical location.
Transforms Images Resampling Registration

## Slide 9: Images
Most non-medical image viewers do not support an-isotropic image spacing:
Transforms Images Resampling Registration

## Slide 10: Images
SimpleITK2Numpy:
  sitk.GetArrayFromImage – Data copied into numpy array (mutable).
  sitk.GetArrayViewFromImage – numpy array view of image data (immutable).
Numpy2SimpleITK:
  Copy bulk pixel data into SimpleITK image: new_image = sitk.GetImageFromArray
  Set all of the parameters defining the physical region in space:
    new_image.CopyInformation
    or
    new_image.SetOrigin, new_image.SetSpacing, new_image.SetDirection
Caution: If the SimpleITK image is released the array view memory is no longer valid.
Transforms Images Resampling Registration

## Slide 11: Resample: Image + Transform
Resampling, three elements (assuming arbitrary interpolation method):
  Image – the image we resample in coordinate system m.
  transformation – T(fp) = mp maps points from coordinate system f to m.
  resampling grid – uniform set of points which will be mapped by the transformation.
f
m
Transforms Images Resampling Registration

## Slide 12: Resample: Image + Transform
Specifying the resampling grid
  Use an existing image.
  Use origin, size, spacing, and direction cosine.
f
m
Unexpected results: errors in resampling grid specification or transformation.
Transforms Images Resampling Registration

## Slide 13: Registration – Coordinate Systems
Three coordinate systems: Fixed, Virtual, Moving.
Three transformations: Tf(vp) = fp
Tm(vp) = mp
Topt(mp) = mp’
Most often Tf=I, the fixed and virtual coordinate systems coincide.
Transforms Images Resampling Registration

## Slide 14: Registration - Framework
Optimizers:
  Exhaustive
  Nelder-Mead Simplex/Amoeba
  Powell
  1+1 evolutionary
  GradientDescent GradientDescentLineSearch RegularStepGradientDescent
  ConjugateGradientLineSearch
  L-BFGS-B
  L-BFGS-2
Similarity metrics:
  MeanSquares Demons Correlation ANTSNeighborhoodCorrelation JointHistogramMutualInformation MattesMutualInformation
Multi-resolution framework.
Masks.
Sampling strategies (NONE, REGULAR, RANDOM).
Transforms Images Resampling Registration

## Slide 15: Registration – Implementing Your Own
Look for a similar example in the notebooks repository.
Start from scratch, start simple (i.e. single scale).
Modify the registration settings by observing the similarity metric value during the iterations using a tight bound on the number of iterations. Modify till you observe desired behavior: (i) consistent reduction in similarity metric value (ii) in an appropriate timely manner.*
* plotting similarity metric value often takes longer than the registration, remove it when done.
Transforms Images Resampling Registration

## Slide 16: Registration – Implementing Your Own
Points to note:
  Initialization - Use domain knowledge, corresponding structures should have some degree of overlap after initialization.
  For the global transformations, SetOptimizerScalesFromPhysicalShift is required as the parameters are not commensurate (except for translation).
  Sampling - Random and uniform sampling reduce computation time.
  Similarity metric – problem dependent, *MutualInformation most generic, MeanSquares most specific and rather limited.
  Use masks to specify ROI. If small mask in large image, change to a cropped image without a mask.
  Optimizers - *Gradient* - best suited for global transformations with small number of parameters. L-BFGS-B use for BSplineTransform, large number of parameters.
Transforms Images Resampling Registration

## Slide 17
Let’s start the tutorial,
off to the races we go:
Wikimedia commons, public domain, race horse filmed by Edward Muybridge 1878.